## Slide 1: Crosstalk on Signal-Return Loops Adinath Phene, Shrinithi Venkatesan
February 29, 2024

## Slide 2
What is Crosstalk?
Different Return Path Geometries
Varying No. of Aggressors
Best Design Practices
Agenda

## Slide 3
Changing current in the aggressor loops creates changing magnetic field.
Changing Magnetic field in Aggressor Loop induces voltage in the victim line.
Crosstalk
M = mutual loop inductance between Aggressor & victim loops
n = Number of simultaneously switching aggressors
= current change in each aggressor
dt = rise or fall time of the aggressor
Victim Trace
Aggressor Trace

## Slide 4
Shared & Separate Return Traces
Use a 10x probe
Use spring tips
Continuous Return Trace
Equivalent circuit
Separate Return Trace
Equivalent circuit

## Slide 5
Crosstalk with Common & Separate Return Traces
Vertical Scale: 500mV/ div
Trigger at Pin 13
Crosstalk on Victim
Common Return Trace
Crosstalk on Victim
Separate Return Trace
Horizontal Scale: 50ns/ div
Vertical Scale: 500mV/ div
Vertical Scale: 2V/ div
Crosstalk on victim line reduces using separate return trace.
More crosstalk observed on the falling edge as compared to the rising edge.
Return Path Geometry | Crosstalk (in mV)
Common Trace | 870
Separate Traces | 180
870 mV
455 mV

## Slide 6
Continuous Return Plane

## Slide 7
Crosstalk with Continuous Return Plane
Trigger at Pin 13
Crosstalk on Victim
Horizontal Scale: 50ns/ div
Vertical Scale: 2V/ div
Vertical Scale: 10mV/ div
Continuous return plane shows least crosstalk on the victim line.
Best design practice to have continuous return plane in PCB.
Return Path Geometry | Crosstalk (in mV)
Common Trace | 870
Separate Traces | 180
Continuous Return Plane | 18
18 mV
12.5mV

## Slide 8
No. of Simultaneously Switching Aggressors
Common Return Trace
Separate Return Traces
Trigger at Pin 13
Trigger at Pin 13
Crosstalk on Victim
Crosstalk on Victim
Horizontal Scale: 50ns/ div
Horizontal Scale: 50ns/ div
Vertical Scale:
2V/ div
Vertical Scale:
2V/ div
1.6 V
1.2 V
347 mV
350 mV
Vertical Scale:
1V/ div
Vertical Scale:
200mV/ div

## Slide 9
No. of Simultaneously Switching Aggressors
Continuous Return Plane
Crosstalk on Victim
Horizontal Scale: 50ns/ div
Vertical Scale:
2V/ div
Trigger at Pin 13
Return Path Geometry | Crosstalk (in mV) | Crosstalk (in mV)
Common Trace | 870 | 1600
Separate Traces | 180 | 350
Continuous Return Plane | 18 | 163
128 mV
163 mV
Vertical Scale:
200mV/ div
Crosstalk increases with increase in the number of aggressors.
Continuous return plane shows least crosstalk on the victim line.

## Slide 10
Do not share return paths between the signal-return loops of the aggressor and victim. Use a separate return conductor.
Reduce the loop mutual inductance between aggressor and victim signal-return paths by keeping the loops far apart.
Reduce the number of simultaneously switching signals which have mutual inductance to the victim loop.
Use a Continuous Return Plane on a PCB to reduce the self-inductance in the signal-return path and mutual loop inductance between aggressor and victim traces.
Best Design Practices to Reduce Crosstalk:

## Slide 11
Questions?